## Slide 1: Uncertainty Assessment Using Reservoir Simulation Models – Practical Guidelines
Anil Ambastha
Chevron Nigeria Limited
March 31, 2014

## Slide 2: Outline
Introduction to experimental design (ED)
Selection of uncertain parameters and their ranges
Response or tracking functions (or variables)
Uncertainty assessment using ED
Development of multiple history-matched models – A case study
Uncertainties for forecasting situations
Concluding remarks
ED is a practical way to assess uncertainty
using reservoir simulation models.

## Slide 3: ED Introduction - Setting the Stage
  Each “empirical” relationship requires data from “experiments”
    SWIR = a – b log (k)
    log (k) = a + b f
    RF = 0.114 + 0.272 log (k) + 0.256 Swi – 0.136 log (mo) – 1.538 f – 0.00035 h
    y = ao + (a1 x1 + a2 x2 + …) + (a12 x1 x2 + a13 x1 x3 + …) + (b1 x12 + b2 x22 + ….)
    x1, x2 etc. may be complex transforms (log, sin, exp, etc.) of the underlying Variable
More complex the relation => More coefficients to evaluate => More experiments needed to generate required data

## Slide 4: ED Introduction - Basic Terms
  Parameters (Variables, Factors) – Uncertain x’s
  Levels (Ranges) of Parameters – Values x’s can assume
  Response variable – y to either optimize (minimize) or evaluate via regression.
  Response equation (Proxy equation, Surrogate function) – Equation for y as a function of all x’s with all coefficients evaluated via data from experiments.
    Can sample this equation via Monte Carlo simulation after specifying probability distribution functions for all x’s
Experimental Design – Systematic, statistical method to uncover relationship between y and x’s that cannot be reasonably handled by “One-Variable-at-a-Time” (OVAT) approach.

## Slide 5: ED Introduction - Experimental Design Methods
  For K factors at L levels:
  Plackett-Burman (1946) design - Experiments in multiple of 4 (e.g., 12 experiments to screen upto 11 factors)
    Center-point case adds one more experiment.
    Folded Plackett-Burman design - Twice as many experiments as the original Plackett-Burman design
  Full Factorial design - LK experiments
    7 factors at 3 levels each = 37 = 2,187 experiments
    Solution – Use D-Optimal or Box-Behnken Design
Plackett-Burman and D-optimal designs are sufficient.

## Slide 6: Selection of Uncertain Parameters and Their Ranges
  Capture all important uncertainties (Use G&G and PE Knowledge)
    Screen for “heavy-hitters” using Plackett-Burman Design .
  Develop “realistic” ranges for parameters
    Not too wide and not too narrow
    Avoid “anchoring” effect
  Keep recovery mechanism and/or study objectives in mind to select relevant parameters
Do not just stop at 7 or 11 uncertainties.

## Slide 7: Typical Ranges for Relative Permeability Parameters based on Corey Equation Representation for Water-Wet System
Parameter | Typical Range
krocw (with kbase = kabsolute in line with earth models) | 0.7-1
krwro | 0.05-0.5
krgro | 0.1-0.7
Sorw (or Sorg) | 0.1-0.35
Sgc | 0-0.05
nw (now, nog or ng) | 1.5-5
Land’s constant (if residual saturations are modeled using Land’s equation) | 2-5
SWIR of earth model is NOT a separate parameter!!!

## Slide 8: Response or Tracking Functions (or Variables)
OOIP (when “static” parameters, OOWC, OGOC, and/or PVT affecting OOIP are involved)
Cumulative oil production at the end of history
Breakthrough times for selected wells
Mean square error (MSE) functions for simulated vs. actual:
  static pressure difference
  RFT (MDT) pressure difference (if available)
  water cut (or WOR) or cum. water production difference
  producing GOR or cum. gas production difference
Data QC - Key to select “representative” data to develop response functions/variables

## Slide 9: Response Function – Unintended Consequences (Simplified Data from Chen and Oliver, SPE 164902)
MSE = Sum over data points [(Simulated data – Observed data)^2/(Data error variance)]
Data error standard deviation = 2 bar and 100 m3/day for RFT pressure and oil rate, respectively
Two observed data points:
  RFT pressure = 250 bar, oil rate = 4,000 m3/day
Two answers for error = (simulated data – observed data):
  RFT error = 20 bar (8%), oil rate error = 400 m3/day (10%)
  RFT error = 8 bar (3.2%), oil rate error = 1,000 m3/day (25%)
One value for MSE = 116
Combine various items in one error function at your own risk!

## Slide 10: Uncertainty Assessment Using ED
  Develop initial set of parameters and their ranges for “pressure and saturation matching”, history-match (HM) error files and tracking variables.
  Use Plackett-Burman design to screen for “heavy hitters”.
  Develop final set of parameters and their ranges based on results from Step 2.
  Use D-optimal design with parameter set from Step 3.
  Develop and check adequacy of proxy equations for HM errors and tracking variables.
  Run Monte Carlo simulation using proxy equations.
  Filter Monte Carlo simulation runs using appropriate criteria.
  Make simulation runs for filtered cases from Step 7.
  Select “acceptable” HM cases by analyzing answers for HM errors and tracking variables, and plotting field-level and well-by-well results.
Follow a systematic process. Iterations may be required!

## Slide 11: Development of Multiple History-Matched Models – A Case Study
  Brownfield with 45 years of history by 2010
  13 years under peripheral water injection since 1997
  160 wells (including 44 horizontal producers and 19 injectors)
  5 major reservoirs
  516 RFT pressure data points for 49 wells over 22 years
  3-D, 3-phase, black-oil system
Full-field problem with large amount of data

## Slide 12: Development of Multiple History-Matched Models - “Heavy hitters” for RFT Error
Pareto chart is sufficient to visualize “heavy hitters”.

## Slide 13: Development of Multiple History-Matched Models - “Heavy hitters” for Cumulative Oil Production at the End of History
“Heavy hitters” can and do change for different variables.

## Slide 14: Development of Multiple History-Matched Models - Proxy Equation Adequacy Check for RFT Error
Did you note an “extreme” test data point? Have a large enough “test” data set.

## Slide 15: Development of Multiple History-Matched Models - Proxy Equation Adequacy Check for Cumulative Oil Production at the End of History
Unbiased assessment of proxy equation adequacy is important.

## Slide 16: Development of Multiple History-Matched Models - Filtering of Monte Carlo Simulation Cases
84 cases
Filter, but verify. Run actual simulation and analyze results again!

## Slide 17: Development of Multiple History-Matched Models - Cross-Plots for RFT Errors
Example of an
unacceptable case
MSE = 9842 psi2
MSE = 6624 psi2
MSE = 6055 psi2
MSE = 29461 psi2
Rejected later
Acceptable
Acceptable
Full analysis makes your product robust.

## Slide 18: Uncertainties for Forecasting Situations
  Well – Constraints and limits, flow tables
  Operations/Surface facilities – Constraints and limits, operational downtime, artificial lift, “put-on-production” schedule
  Development opportunities – Workover timings, zone switch, infill wells, recovery mechanisms
  Fields - Timing
Look at the BIG picture! Involve all stakeholders.

## Slide 19: Concluding Remarks
  Logical description of uncertainty assessment steps
  Practical tips and guidelines
Always remember one thing – No matter how careful we are, we cannot assess the impact of “unidentified” uncertainty.

## Slide 20: BACK-UP

## Slide 21: Typical “Dynamic” Uncertain Parameters
Aquifer specifications (cells representing aquifer i.e., aquifer direction and extent, aquifer pore volume multipliers, and aquifer transmissibility multipliers)
Relative permeability parameters
Permeability multipliers
kv/kh
Transmissibility multipliers in x-, y- or z-direction to represent barriers/baffles/ “shale”/stratigraphic compartments
Regional (or local) adjustment parameters related to any property such as permeability, porosity, residual saturations, PI, skin, etc. (CAUTION – Ideally, minimize use of such parameters, especially local ones)
Fault parameters (length, vertical extent, transmissibility)
Formation compressibility
PVT
Initial reservoir pressure (sometimes)

## Slide 22: Tornado Diagram for “Heavy hitters”
Tornado diagram can also be used to identify “heavy hitters”.