## Slide 1
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl

## Slide 2
Fiber Optic Sensing Improves Unconventional Reservoir Development
Trey Lowe
Devon Energy
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl

## Slide 3
Agenda
Unconventional wells and the field development challenges
Fiber optic sensing
Example data set
Using the data to improve models
Conclusions

## Slide 4
Unconventional Development
Tightly spaced horizontal wells
  Normally 5,000 to 10,000-ft (1500 to 3000-m) horizontals
  Well spacing between 150 to 900 ft (45 to 275m)
Multi-stage fracturing
  10 to 40 stages with 3-6 clusters

## Slide 5
Need to Optimize Completions
What is our frac geometry?
How does the rock affect cluster efficiency (distribution of fluids into each cluster)?
How closely should we space our stages and clusters?

## Slide 6
Planning Infill Development of Unconventional Reservoirs
H?
XL?
Well spacing?
Landing interval?
Notes: Another way to visualize it…

## Slide 7
Setting Up an “Underground Laboratory”* to Measure Some of the Unknowns
H?
XL?
Offset pressure monitoring (XL, azimuth)
Vertical well (H)
Fiber optic sensing (# of fracs, relative size of each frac)
Microseismic / Tiltmeters (XL, H, and azimuth)
*Source: D. Koskella, Noble Energy, 2014

## Slide 8
Fiber Optic Sensing

## Slide 9: A Way to Answer the Questions: Fiber Optic Sensing
Complete an infill well with fiber optics sensing technology
Fiber optic sensing technology
  Distributed Temperature Sensing (DTS)
  Distributed Acoustic Sensing (DAS)

## Slide 10: What is Fiber Optic Sensing?
The fiber is the sensor
Measurement every 3 feet (1m) along the fiber
T9,999
T9,998
T9,997
T1 T2 T3 T4 ……….

## Slide 11
Installing Fiber Optic Cable
Attach fiber optic line to the outside of production casing
Take care when perforating!
  Options: sleeve system or oriented perforating

## Slide 12: Fiber Optic Monitoring Distributed Acoustic Sensing (DAS)
Notes: This is an amazing movie file showing DAS data acquired in real time. This movie will be edited prior to final submission to take out about 30-seconds. It shows what DAS data looks like in real time. There is an example where a cluster is not taking fluid and also shows where a downhole sleeve failed, which can be seen in real-time.
I will have a back-up copy of this presentation which does not include a movie file.

## Slide 13
An Example Data Set
Source: SPE 166295, 2013

## Slide 14: Distributed Acoustic Sensing (DAS) Stage 5
+
-
Depth
Clusters
Cluster #1 is dominant
Cluster #2 is not accepting any fracturing fluid
-
+
Time

## Slide 15: Distributed Temperature Sensing (DTS) Stage 5
+
-
Depth
Once again…
Cluster #1 is dominant
Cluster #2 is not accepting any fracturing fluid
-
+
Time
Clusters
Blue is cool, Red is warm

## Slide 16: Surface Microseismic Setup
Star Pattern
10 runs of 2.5 mi (4km) each
26 mi2 (65 km2) coverage
1476 geophone stations
Very useful real-time results

## Slide 17: Surface Microseismic Data Stage 5
Once again…
Cluster #1 is dominant
Cluster #2 is not accepting any fracturing fluid

## Slide 18: RA Tracer Log Stage 5
Clusters
Once again…
Cluster #2 is not accepting any fracturing fluid

## Slide 19: Production Log (PLT) Stage 5
Production data corresponds to the fracturing monitoring
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 20
Using the Data to Improve Models
Notes: Now that we have some faith in the measurements, let’s talk about how it can be used to improve our models.

## Slide 21
Improving the Fracture Model using Fiber Optics
Engineers use advanced fracture models to understand frac H and effective XL

## Slide 22
DAS Measurement Improves Fracture Model
The non-informed model predicts this cluster to have XL of 2,500-ft
Use the data
The improved model uses fiber optic DAS data to restrict the model – minimal H, XL and proppant placement
-
+
Depth
+
-
XL
+
-
XL

## Slide 23
Microseismic Data Improves Reservoir Simulation
The above model uses assumed planar fracture geometry
*Source: SPE 168596, 2014, Cipolla, et al. Hess
Use the data
The improved model uses microseismic events to constrain the DFN model
Fracture area = 36MM ft2
Fracture area = 30MM ft2

## Slide 24
Microseismic Data Improves Reservoir Simulation
Pressure distribution after 10-years for a “text book” planar frac model
Use the data
Pressure distribution with improved model
Now we can make better decisions about well and cluster spacing!

## Slide 25
Conclusions
Fiber optic sensing is a powerful addition to the “underground laboratory” and is being used to optimize fracturing models
The integration of advanced fracture monitoring are a clear path to optimized well spacing, landing interval and completion design.

## Slide 26
Acknowledgements
SPE Distinguished Lecturer Program
Devon Energy
My wife and children
My Devon family (Dan Wood, Breanne Kennedy, Mike Potts, Jim Heinze, and many others)
Industry friends and colleagues (J. Miskimins, A. Daneshy, K. Banks, H. Allen, B. Shroyer, and others)

## Slide 27
Questions?