## Slide 1
Increasing Production with Better Well Placement in Unconventional Shale Reservoirs - Challenges and Solutions
Jason Pitcher
Director – Business Development CamShale Completions
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl

## Slide 2
Presentation Outline
What happens when you assume the “frac will get it”
Current Best Practice in North America
Geomechnical Properties that affect Production
Using Data through the Life Cycle
  Drilling
  Completion
  Stimulation
Discussion Points
Advances from 2012 / 2013

## Slide 3
What happens when you assume the “frac will get it”
Modeland, N., Buller, D. and Chong, K.K. 2011. Statistical Analysis of Completion Methodology on Production in the Haynesville Shale. Paper SPE 144120 presented at the SPE North American Unconventional Gas Conference and Exhibition, The Woodlands, Texas, 14-16 June
8 Month Cum vs # of Stages (Entire Play)
Non Core
Area
Core Area
8 Month Cum vs # of Stages (Core Area)
Core Area
8 Month Cum vs # of Stages (Bull Bayou Field)
Core Area

## Slide 4: Old Problem Old Solution
1998

## Slide 5
Presentation Outline
What happens when you assume the “frac will get it”
Current Best Practice in North America
Geomechnical Properties that affect Production
Using Data through the Life Cycle
  Drilling
  Completion
  Stimulation
Discussion Points
Advances from 2012 / 2013

## Slide 6
Notes: 6

## Slide 7
Drill an Evaluation Well
Open Hole Logging
Coring
  Characterize the Reservoir
  Define the Target
Dfit or MiniFrac
Notes: 7
Accurate identification of organic rich, gas prone, and permeable zones
Rock Mechanics for wellbore stability and horizontal drilling and clay type for fluid sensitivity
Fracability (brittleness): Geomechanical and Geochemical consideration for Frac Fluid Choice, proppant selection and hydraulic rates and Volume.

## Slide 8
Drill a Horizontal / High Angle Well
LWD consists of Gamma Ray
Well is geosteered to stratigraphy
Pattern match gamma response to offset logs
SPE 152580
Notes: 8
Placing the well in the zone that will deliver maximum value after stimulation (biggest bang for the buck) is the goal. If you only evaluate after drilling, you have no control over what rock the well is in – you have whatever the well construction team has delivered.

## Slide 9
Complete the Well
Equally spaced packers or perf intervals
Spacing between intervals has been decreasing from 400’ (122m) to as low as 100’ (30m).
Notes: 9
Use Data acquired during the drilling process to improve the success of zonal isolation. This gives you the potential of customizing the completion string before it’s run in the ground. If you instrument it, you are setting up monioring systems for long term productivity mapping and for completion / stimulation program validation.

## Slide 10
Stimulate the Well
Stimulation Design is a one size fits all approach, iterated on empirical data.
Notes: 10
Use the acquired data to fine tune and develop the stimulation program. Validate the program using instrumented completion and microsiesmic.

## Slide 11
Presentation Outline
What happens when you assume the “frac will get it”
Current Best Practice in North America
Geomechnical Properties that affect Production
Using Data through the Life Cycle
  Drilling
  Completion
  Stimulation
Discussion Points
Advances from 2012 / 2013

## Slide 12: Shale Brittleness Index
Rickman et al. Paper SPE 115258
Notes: Brittleness is the measure of
12

## Slide 13: Rock Mechanics from Sonic
Dynamic Young’s
modulus
Poisson’s ratio
Convert to Static:
Brittleness Index:
Rickman et al. SPE 115258
Mullen et al. SPE 108039

## Slide 14: For Anisotropic Media:
Mavko, G. et al. The Rock Physics Handbook 2009
Buller, D. et al. 2010 SPE 132990
Petrophysical Evaluation for Enhancing Hydraulic
Stimulation in Horizontal Shale Gas Wells

## Slide 15: Brittleness Index vs Gas Production
Post Frac Production Log – day 45, well flowing 9MM
Buller, D., Suparman, F., Kwong, S., Spain, D. and Miller, M. 2010. A Novel Approach to Shale-Gas Evaluation Using a Cased-Hole Pulsed Neutron Tool.
Notes: Indeed there was a variation in frac performance when we look at Brittleness Index plotted against frac stges and individual perf clusters. There is an obvious correlation of more gas produced from ares of higher porosity and higher Brittleness Index.

## Slide 16: Frac Results
Higher Clay Interval
Near WellBore Region
3’ (1m)
Lower Clay Interval
Buller, D. et al. 2010 SPE 132990
Petrophysical Evaluation for Enhancing Hydraulic
Stimulation in Horizontal Shale Gas Wells
Notes: Near wellbore governs all frac mechanics and production
  Influences Injection Pressure
  Pad and proppant Entry
  Pressure drawdown during flowback
Summary high clay interval properties
  Smaller effective fracture width and less height growth
  Increased likelihood of screenout
  Lower gas production
  Higher propensity for proppant embedment
Summary lower clay interval properties.
  Wider effective fracture width and better height growth
  Better ability to place proppant and achieving higher complexity
  Better gas production and less risk of proppant embedment

## Slide 17: Haynesville #1
Buller, D. et al. 2010 SPE 132990
Petrophysical Evaluation for Enhancing Hydraulic
Stimulation in Horizontal Shale Gas Wells
Notes: In this example, the brittleness and frac index (frac index is brittleness modified by sonic layering anisotropy) are quite good. The well took almost all designed proppant load and exhibits good production in all stages. This is a good well.

## Slide 18: Haynesville #2
Prop 62.2%
Prop 85.3%
Prop
79%
Prop
29.5%
Prop 2.6%
Prop
89.5%
Prop 100%
Prop 3%
Prop 35%
Prop 55.4%
768
376
0
0
0
0
0
0
0
0
0
162
15
379
64
137
298
1
0
0
0
0
0
0
0
301
0
214
67
1
137
0
0
0
100
768
266
0
7
408
Buller, D. et al. 2010 SPE 132990
Petrophysical Evaluation for Enhancing Hydraulic
Stimulation in Horizontal Shale Gas Wells
Notes: In this Haynesville example, it is clear that this well has problems. Only 6 of the 10 stages took >50% designed proppant load and the corresponding production per cluster (red arrows) is poor. The Frac index and brittleness index clearly show that this well is in poor quality rock for greater than 50% of it’s length.

## Slide 19
Haynesville #1 – 9 of 10 Water Fracs Placed – PL rate 8.2 MMCF/D
Haynesville #2 – 6 of 10 Fracs Placed > 50% – PL rate 4.5 MMCF/D

## Slide 20
Presentation Outline
What happens when you assume the “frac will get it”
Current Best Practice in North America
Geomechnical Properties that affect Production
Using Data through the Life Cycle
  Drilling
  Completion
  Stimulation
Discussion Points
Advances from 2012 / 2013

## Slide 21: Horizontal Cased Hole Pulsed Neutron Log – Haynesville Shale
Brittleness Index, Fracture Ease, Effective Porosity, Free Gas, & TOC
Horizontal In & Out of Primary
Target Interval
Free Gas
Stress
Fracture
Ease
Brittleness Index
Lithology
Effective
Porosity
CHI Model Triple Combo Data
Notes: 21

## Slide 22: Horizontal Cased Hole Pulsed Neutron Log – Haynesville Shale
Evenly spaced stages
Unevenly spaced stages
Notes: 22
Stage sizes and location along the lateral should be based on the formation encountered. In this example the toe stages are in poorer quality rock and frac stages and perforation sets should consider this. Fracs should target the free gas and avoid the most ductile rock where proppant will embed. This may result in fewer perf sets. The heel stages are in better rock and uniform frac stages can be considered.
Crosslinked gel should be considered to maximize proppant placement and maintaining a good fracture / wellbore connection.

## Slide 23: Haynesville #2
Prop 62.2%
Prop 85.3%
Prop
79%
Prop
29.5%
Prop 2.6%
Prop
89.5%
Prop 100%
Prop 3%
Prop 35%
Prop 55.4%
768
376
0
0
0
0
0
0
0
0
0
162
15
379
64
137
298
1
0
0
0
0
0
0
0
301
0
214
67
1
137
0
0
0
100
768
266
0
7
408
Notes: In this Haynesville example, it is clear that this well has problems. Only 6 of the 10 stages took >50% designed proppant load and the corresponding production per cluster (red arrows) is poor. The Frac index and brittleness index clearly show that this well is in poor quality rock for greater than 50% of it’s length.

## Slide 24: Haynesville #2
Prop 62.2%
Prop 85.3%
Prop
79%
Prop
29.5%
Prop 2.6%
Prop
89.5%
Prop 100%
Prop 3%
Prop 35%
Prop 55.4%
768
376
0
0
0
0
0
0
0
0
0
162
15
379
64
137
298
1
0
0
0
0
0
0
0
301
0
214
67
1
137
0
0
0
100
768
266
0
7
408
Notes: In this Haynesville example, it is clear that this well has problems. Only 6 of the 10 stages took >50% designed proppant load and the corresponding production per cluster (red arrows) is poor. The Frac index and brittleness index clearly show that this well is in poor quality rock for greater than 50% of it’s length.

## Slide 25: Shale Completion Strategy: Based on Formation Brittleness Index
Low
High
Low
High
Low
High
Proppant Concentration
Fluid Volume
Proppant Volume
Youngs Modulus
7 E 6
6 E 6
5 E 6
4 E 6
3 E 6
2 E 6
1 E 6
SPE 115258
Haynesville
Marcellus
Barnett
Eagleford
Hybrid
Notes: 25
When the rock is more ductile (low YM) like the Eagle Ford, the proppant concentrations need to be higher (embedment), placed in the formation with less fluid (Hybrid or Conventional with even more xlinked fluid), and an even higher volume of proppant to insure good conductivity............especially if the hydrocarbon production is liquid (oil)

## Slide 26
Shale / Prop Interface
Proppant
Proppant
Extruded
Shale
Shale Stimulation Strategy – what are we trying to do?
Pitcher, J. and Buller, D., 2011 Shale Assets: Applying the Right Technology for Improving Results. Paper presented at the AAPG International Convention and Exhibition, Milan, Italy, 23-26 October.

## Slide 27
Presentation Outline
What happens when you assume the “frac will get it”
Current Best Practice in North America
Geomechnical Properties that affect Production
Using Data through the Life Cycle
  Drilling
  Completion
  Stimulation
Discussion Points
Advances from 2012 / 2013

## Slide 28
Discussion Points
Shale reservoirs are statistical plays
  Current Practice has limitations
Well placement strategy dictated by geomechanics
Geosteering enhances production by maximizing fracable reservoir contact
Data acquired while drilling has a long shelf life
  Data used in completion and stimulation optimization
  Used in reservoir scale production models

## Slide 29
Presentation Outline
What happens when you assume the “frac will get it”
Current Best Practice in North America
Geomechnical Properties that affect Production
Using Data through the Life Cycle
  Drilling
  Completion
  Stimulation
Discussion Points
Advances from 2012 / 2013

## Slide 30: Advances from 2012/13
“Operators are using more sand per stage and packing more stages closer together in each lateral”
E&P Magazine July 2014
“There’s a tendency toward super fracs. UG in particular has shown that by increasing proppant loading, well IP rates can be vastly affected positively.”
Rob Fulks, Director of Shale Resource Projects and Pressure Pumping Services, Weatherford
SPE 170764 – Pioneer – EFS 2014
But over the past year or so,
drillers have determined that
using larger amounts of sand in
fracking can lead to much better
energy production. That has led to surging demand for Emerge Energy's sand and soaring shares.
IHS data show that EOG has about quadrupled the volume of proppant it is pumping from around 0.4 million pounds of proppant per 1,000 lateral feet in 2012 to 1.5—2.0 million pounds since 4Q 2013. EOG’s wells showed a positive correlation between larger volumes of proppant and higher average peak month production rates.
2nd Bone Springs thoughts (E&P $696) – Expecting strong revisions to type curves by YE on enhanced completions. Generally, proppant volumes have increased from 600-700lbs per foot to 1,100-1,500lbs with leading edge tests at 2,500lbs. Stage spacing has also moved to 250-300ft down from 400-500ft. Early results have been extremely encouraging with 30d IPs up 50-70+% y/y.
Notes: Downspacing Laterals, downspacing stages, increasing proppant loads – all designed to increase productivity and overcome the inherent failings of the machine.

## Slide 31
Thank You
Спасибо
Gracias
Merci
谢谢你
Grazie
Takk
شكراً جزيلاً
Sağol
ありがとう
Obrigado
Jason Pitcher
Director - Business Development CamShale Completions
Cameron